## Slide 1: 16b CPU – V2
Capacités de l’architecture &
Implémentation de la micro-architecture

## Slide 2: Nouvelle Architecture
Bénéficier d’instruction R et I avec tous les registres possibles
Passer à 16 registres (PC exclu), 4 spéciaux + 12 généraux (préc. 8)
Les instructions R resteraient sur 1 mot ; 16 instructions seraient alors disponibles.
Des instructions Immediate qui seraient de 2 types :
  Accumulate Only ( Imm=0), sur 1 mot
  Immediate on full word ( [-32768, +32767]), sur 2 mots
Les instructions de JUMP et BRANCH resteraient sur 1 mot à l’exception de JAL, afin de prévoir des appels à des fonctions très éloignées en mémoire.

## Slide 3: Nouvelle Architecture R-type arch.
0 opcode (3)  ALUctrl (3) dst (4) src1 (4) src2 (4)
ADD-XOR (0x0-0x4)
RESERVED (0x5-0x7)
R3-type
Property: dst cannot be $0, as it is unalterable!
NOP (0x0)
CMP (0x1)
MOV (0x2)
RESERVED (0x03)
0 0 opcode (2)  ALUctrl (3) 0000 src1 (4) src2/dst (4)
R2-type : batch1

## Slide 4: Nouvelle Architecture R-type arch.
SLL (0x01)
SRL (0x02)
SRA (0x03)
RESERVED (0x00)
0 1 opcode (2)  ALUctrl (3) 0000 src1 (4) src2/dst (4)
R2-type : batch2

## Slide 5: Nouvelle Architecture I/J-type arch. 1w, R0
Branch-type (1w, R0)
1 00 opCode(2) Signed Immediate (11)
BZ (0x0)
BNZ (0x1)
BLT (0x2)
BLE (0x03)
Jump-type (1w, R0)
1 01 0 opCode(1) Signed Immediate (11)
JI (0x0)
BCF (0x1) : Branch if Carry Flag

## Slide 6: Nouvelle Architecture I/J-type arch. 1w, R2 (1dst + 1src + 1Imm[4])
R2/MEM-type (1w, R2)
1 10 opCode(1) Imm(4) src1(4) src2/dst (4)
lw (0x0)
sw (0x1)
Exemples :
Sw WD2, Imm+A2 (reg, mem address)
LW AW, Imm+A2 (reg, mem address)

## Slide 7: Nouvelle Architecture I/J-type arch. 1w, R1 (1src + 1Imm[4]) or R2
R1-type + R2/ALU-type (1w, R1 or R2)
JR (0x0)
ADDa (0x1)
1 01 1 opCode(1) Imm(7) src1/src1+dst (4)

## Slide 8: Nouvelle Architecture I/J-type arch. 2w
2w-type
1 11 aluCtrl(3) opCode(2) src1(4) dst (4)
JAL (aluCtrl=0x0, opCode=0x0) : dst=$ra
ALUi2 (aluCtrl=0x0-0x4, opCode=0x1) : src1, dst
LODi2 (aluCtrl=0x0, opCode=0x2) : src1=$0, dst
CMPi2 (aluCtrl=0x1, opCode=0x3) : src1
Immediate (16)
TODO : Add Jump Immediate on 16b with automatic decision by assembler script (7b version or new 16b).

## Slide 9: micro-architecture V2
Register File
16
A2 (4)
A1 (4)
Inst [7:4] (Src1)
R1
R1 or PC
PC’’
R2
R2 or SE
dstInSrc2
B
A
0,ALU ctrls
REG
Write
PC’
RAM Out
ALU Out
R1
WD
Write Src
PC
MIR
Intr [15:0]
PC
PC load
SRAM
RAM Write
PC/A1
RD1
New Instr
PC Capture (O)
MEM Capture
R1 Capture (O)
WD2
ALU flags
PC count
REG
Capture
Update flags
Sign-extend 4  16
Inst [11:8]
Sign-extend 11  16
Inst [10:0]
Sign-extend 7  16
Inst [10:4]
R0 or R1w or R2w or i2
SE
res
ALU Capture
Inst [3:0]
(Src2/Dst(R3)/Src1(R1w))
src1InSrc2
PC
AW (4)
Inst [11:8] (Dst/N.A.)
ALU/A2
RD2
R1
RD2
ALU

## Slide 10: Register File Organisation
$0 : 0x0000
$GP : Global Pointer (variables visible from anywhere within the program).
$SP : Stack Pointer (points to 1st free stack memory location)
$BP : Base (or Frame) Pointer ($BP <= $SP)
$RA : Function Return Address
$s0 (callee-preserved)
$t0 (temporary registers)
$t1
$s1
$t2
$t3
$v0 (return values of a procedure)
$v1
$a0 (input arguments to a procedure)
$a1
$a2

## Slide 11: Controls logic handles V2
PC Capture | PC Count | src1 In Src2 | dst In Src2 | R0 / R1w / R2w / i2 | R1 Capture | R1 or PC | R2 or SE | ALU Ctrls | update Flags | RAM Write | WriteSrc | REG Write | PC Load
1 | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 3 | 1 | 1 | 2 | 1 | 1
Table des actionneurs et taille en bits associée
Total : 14 actionneurs commandables, sur 18 bits